## Slide 1: EE2 Circuits and Systems Problem Class 3 Lab 1 & 2 Explained
Prof Peter Y. K. Cheung Imperial College London
URL: www.ee.ic.ac.uk/pcheung/teaching/EE2_CAS/ E-mail: p.cheung@imperial.ac.uk
Notes: Welcome to this first course you will take on electronic engineering. I am looking forward to teaching such a course to Design Engineering students for a long time. It presents a personal challenge: how to select and teach from a vast amount of materials we normally teach to first year EE students to you in a quarter of the available time? Even more challenging is: how to ensure that you retain what you learn in electronics for years to come, and only encounter this topic rarely during this period? I am going to give this a try.
Because this is a new course and I am giving it for the first time, I would welcome feedback from you in any form.
All my teaching materials including lecture slides with notes, laboratory work and tutorial problem sheets can be found on the course webpage shown here. Furthermore, all lectures will be recorded with Panopto.

## Slide 2: Task 1 – Output impedance of PicoScope SigGen
Iout (output current)
Rs
40
Ideal – constant Rs
Actual

## Slide 3: Task 2 – Using a Unity Gain Amplifier (2)
Add R3 (200k) – makes no difference, but ready for Task 3

## Slide 4: Task 3 – x4 Amplifier Failure (1)
Add R4. The gain of the amplifier should be x4.
However, you will see that V1 shows a sine wave with top of it “clipped”.

## Slide 5: Task 3 – x4 Amplifier Success (1)
Add C2 and C3. This will now work. Why?

## Slide 6: Task 3 – x4 Amplifier Success (2)
Consider what happens at DC source (principle of superposition):
C2 is open-circuit, so 2.5V dc is blocked by C2. Instead, V+ is now at 2.5V because of R1 and R2 (voltage divider).
C3 is open-circuit. Therefore the op-amp is now a x1 amplifier as in Task 2.
2.5V
x1
2.5V

## Slide 7: Task 3 – x4 Amplifier Success (3)
Consider what happens at high frequency (e.g. 10kHz sine wave):
C2 is short-circuit, so VG goes directly to V+.
C3 is short-circuit. Therefore the op-amp is now a x4 amplifier

## Slide 8
Bias voltage at pin 3 is poor because ……
Task 4 – Better bias circuit (1)

## Slide 9: Task 4 – Better bias circuit (2)
Replace resistor divider bias circuit with proper voltage reference
Why is R3 necessary?
What is the loading seen by the PicoScope signal generator?

## Slide 10: Task 5 – Large Gain amplifier failure
Replace R1 with 2k ohm resistor. Gain = 1 + R2/R1 = 101

## Slide 11
Gain drops by 20dB /decade 1st order
Gain = 0dB at around 1MHz
Gain-Bandwidth Product (GBP) = Gain x frequency
GBP for MCP6001 is 1MHz
MCP6001
112dB gain up to 2Hz
Task 5 – Gain-Bandwidth Product limit
Notes: Although the open-loop gain of the MCP6001 at DC (or 0Hz) is very high (at over 100,000), this gain drops off very quickly as the signal frequency is beyond 2Hz. Beyond 2Hz, the gain falls off at a rate of -20dB/decade (i.e. drops by a factor 10 as signal frequency goes up by a factor of 10).
As we reach around 1MHz, the open-loop gain is only 1. That means at this frequency, the op-amp, without feedback, will not behave like an amplifier any more.
The frequency at which the gain drops to 1 is known as the Gain-Bandwith Product (GBP). Notice that beween 2Hz and 1MHz, the open-loop gain and the signal frequency, when multiplied together, is a constant = 106.
In other words, given the maximum frequency of your signal that you need to amplify, the GBP tells you how much gain you can obtain from this op-amp. For example, If your maximum signal frequency is 10kHz, you will not be ablet o design an amplifier that gives a gain of at most 40dB (x100), actually will be somewhat lower than x100. You will be exploring this in Lab 1.
There are op-amps designed to have much higher GBP than this is one. However, the higher the GBP, the more likely the op-amp will oscillate (i.e. go unstable). For these op-amp to work, one would need to design the PCB carefully to avoid unexpected feedback path for signals.

## Slide 12: Task 6 – High gain amplifier in 2 stages (1)
Stage 1: non-inverting amplifier with GAIN = 21
Replace R1 with a 10k ohm resistor. Now gain is x21

## Slide 13: Task 6 – x210 amplifier in 2 stages (2)
Stage 2: inverting amplifier with GAIN = -10 (circuit in RED)
Now check Vo1 and Vo2
Topic 11 slide 8

## Slide 14: Task 7 – Audio Amplifier for 8 ohm speaker
Op-amp only can only deliver at most 20mA current at its output
Need special amplifier to drive 8 ohm speaker
Use special amplifier for this purpose

## Slide 15: Lab 2 Task 1 – Half-wave Rectifier
Good half-wave rectifier

## Slide 16: Lab 2 Task 1 – Full-wave rectifier
Poor full-wave rectifier

## Slide 17: Lab 2 Task 1 – Peak detection
Peak detecting

## Slide 18: Lab 2 Task 1 – Sound level detection
R9 – estimate or measure, not easy to calculate

## Slide 19: Lab 2 Task 2 – Comparator with hysteresis

## Slide 20: Lab 2 Task 2 – Comparator to detect sound

## Slide 21: Lab 2 Task 3 – Function Generator

## Slide 22: Lab 2 Task 4 – Lowpass filter

## Slide 23: Lab 2 Task 5 – Pulse-width modulator

## Slide 24: Lab 2 Task 5 – Pulse-width modulator